## Slide 1
Motivation
~1,500,000 culturally deaf in the United States and Canada [1][2] with no efficient and natural way to communicate with the hearing
Communication barriers between sign language speakers and the general populace remain high
Theory
Segments of glove sensor data get converted into 64 features (maximum absolute deviation of the acceleration, variance of angular acceleration, etc.) best representing the hands’ movements
Every model learns values for relevant constants allowing it to be used for prediction later. These constants are stored in the backend to be used on the go for real-time prediction
Support Vector Machine (highest practical accuracy) uses a kernel trick to transform the data into higher dimensions to make it linear classifiable.
The graph below shows an example of a SVM classifying three classes of data by constructing three hyperplanes in a higher dimension. A similar
Voice Sign Language Translation System
Principle of Operation
Features
Objective
Build a system to allow sign-language speakers to communicate with non-speakers in an unobtrusive and natural way
Support a subset of two sign language dialects, namely American Sign Language and Japanese Sign Language
Design Considerations
Computer vision (requires a camera, very difficult to capture just a person’s hands in changing environments)
Data gloves (very expensive)
Support Vector Machines vs. Naive Bayes vs. Decision Trees (SVM has highest accuracy)
Advantages
Allows users to communicate in sign language in a mobile environment
Portable and minimal setup time
Easily integrated into daily routine
Cheaper than other alternatives
Seamless extension for supporting more signs in the future
Results and Analysis
Machine Learning (ML) models were trained on 100 iterations/sign of three users and used to predict on 100 iterations/sign of one user to calculate accuracy
Logistic Regression and Support Vector Machines (SVM) perform better than other ML models like Naive Bayes and Decision Tree Learning
More the input data, better the accuracy of the models. SVM converges with fewer iterations and a higher accuracy compared to Decision Tree Learning as seen in the graphs below
Acknowledgements
Group Members: Akshay Budhkar, Eliot Chan, Biraj Kapadia, Amish Patel
Consultant: Dana Kulić
Course Coordinator: Dan Davison
[1] "Statistics on deaf Canadians," Canadian Association of the Deaf, 2015. [Online]. Available: http://cad.ca/issues-positions/statistics-on-deaf-canadians/.
[2] T. Harrington, "Deaf population of the U.S. - Local and regional deaf populations," Gallaudet University Library Library, 2010. [Online]. Available: http://libguides.gallaudet.edu/content.php?pid=119476&sid=1029190.
[3] "Plot different SVM classifiers in the iris dataset — scikit-learn 0.18.1 documentation", Scikit-learn.org, 2017. [Online]. Available: http://scikit-learn.org/stable/auto_examples/svm/plot_iris.html.
Gloves
MCU
Wireless Module
Power Source
Sensors
Android
Server
Data Pipeline
UI
Text to Speech
Prediction Algorithm
…
Features
Supports 15 American Sign Language (ASL) signs
Supports ~20% of Japanese Sign Language (JSL) symbols
Theoretical accuracy of over 99%
Weighs under X grams
Can run for more than 10 hour on a single charge
Translation latency less than 500 ms
Bluetooth communication between the gloves and mobile application
Model Name | ASL (15 Signs) | JSL (20% of the symbols)
SVM | 96.3% | 100%
Logistic Regression | 99.6% | 100%
transformation can be imagined for n points
representing n signs in a higher dimension